## Slide 1
MINOR PROJECT SECOND DEFENSE
FETAL ECG SEGMENTATION USING DEEP LEARNING
Efforts by:
UDAY BANSAL (35220802822)
HARSHITA SHARMA (21020802822)
ALVIN K SIJO (02120802822)
KANAK PANDEY (20320802822)
DEPARTMENT OF ELECTRONICS AND COMMUNICATION ENGINEERING, BHAGWAN PARSHURAM INSTITUTE OF TECHNOLOGY

## Slide 2
WHY THIS PROJECT TOPIC?
  FETAL ECG MONITORING PROVIDES CRUCIAL INFORMATION ABOUT THE BABY'S HEART HEALTH, ENABLING EARLY DETECTION OF CONGENITAL HEART CONDITIONS AND DISTRESS.​
  THERE IS A GROWING NEED FOR NON-INVASIVE, ACCESSIBLE, AND ACCURATE FETAL MONITORING TO IMPROVE PRENATAL OUTCOMES FOR MOTHERS AND INFANTS.​
  TRADITIONAL FETAL MONITORING SOLUTIONS OFTEN LACK SENSITIVITY AND MAY NOT PROVIDE DETAILED FETAL HEART WAVEFORMS NEEDED FOR ADVANCED DIAGNOSIS.​
  BY USING DEEP LEARNING, THIS PROJECT TARGETS MORE ACCURATE SEPARATION OF FETAL ECG FROM MATERNAL AND NOISY BACKGROUNDS, IMPROVING CLINICAL RELIABILITY.​
  THE PROJECT SUPPORTS THE FUTURE OF PERSONALIZED, TECHNOLOGY-DRIVEN MATERNAL HEALTHCARE.
LIMITATIONS OF TRADITIONAL MONITORING
  MOST EXISTING METHODS ARE EITHER INVASIVE (FETAL SCALP ELECTRODE) OR OFFER ONLY INDIRECT/AGGREGATE HEART RATE INFORMATION, NOT FULL ECG WAVEFORMS.​
  SIGNAL QUALITY IS OFTEN POOR DUE TO INTERFERENCE FROM MATERNAL ECG AND MOTION, MAKING ACCURATE FETAL ASSESSMENT DIFFICULT.​
  MANY SYSTEMS FAIL TO PROVIDE SUFFICIENT DETAIL FOR DETECTING SUBTLE RHYTHM OR WAVEFORM ABNORMALITIES.​
  COMPLEXITY AND DISCOMFORT OF TRADITIONAL TECHNIQUES LIMIT THEIR USABILITY FOR REGULAR HOME- OR MOBILE-BASED MONITORING.
​
DEPARTMENT OF ELECTRONICS AND COMMUNICATION ENGINEERING, BHAGWAN PARSHURAM INSTITUTE OF TECHNOLOGY

## Slide 3
​
NEED FOR REAL-TIME AND CONTINUOUS MONITORING
  MODERN PRENATAL CARE REQUIRES IMMEDIATE DETECTION OF CHANGES IN FETAL CONDITION TO PREVENT ADVERSE OUTCOMES.​
  CONTINUOUS, REAL-TIME MONITORING ALLOWS FOR EFFECTIVE INTERVENTION DURING SUDDEN EPISODES OF FETAL DISTRESS OR HYPOXIA.​
  HOME-BASED AND REMOTE HEALTHCARE SETTINGS BENEFIT FROM REAL-TIME ALERTS, ENSURING SAFETY OUTSIDE HOSPITALS.​
  CONTINUOUS DATA ENABLES TRACKING FETAL DEVELOPMENT TRENDS, NOT JUST SINGLE-TIME EVENTS.
  REAL-TIME INSIGHT BUILDS CONFIDENCE FOR MOTHERS AND CLINICIANS THROUGH PROACTIVE CARE.
PROBLEM STATEMENT
  CURRENT FETAL ECG MONITORING IS OFTEN INSUFFICIENT FOR EARLY, ACCURATE, AND COMPREHENSIVE DETECTION OF FETAL HEART ISSUES.​
  EXTRACTING FETAL ECG SIGNALS IS CHALLENGING DUE TO OVERLAPPING MATERNAL ECG AND NOISE, ESPECIALLY IN NON-CLINICAL SETTINGS.​
  THERE IS A CLEAR CLINICAL NEED FOR A ROBUST, REAL-TIME FETAL ECG SOLUTION THAT WORKS NON-INVASIVELY AND CONTINUOUSLY.​
  LIMITATIONS OF TRADITIONAL AND EXISTING DIGITAL SOLUTIONS RESULT IN MISSED OR LATE DETECTIONS OF CRITICAL CONDITIONS.
  THIS PROJECT AIMS TO DELIVER A PRACTICAL, HIGH-FIDELITY APPROACH TO FETAL ECG MONITORING THAT CAN BE WIDELY ADOPTED
DEPARTMENT OF ELECTRONICS AND COMMUNICATION ENGINEERING, BHAGWAN PARSHURAM INSTITUTE OF TECHNOLOGY

## Slide 4
Fetal ECG (FECG) is used to record the baby’s heartbeat from the mother in a safe, non-invasive way. The baby’s signal is very weak and gets mixed with the mother’s heartbeat and outside noise, so it needs to be cleaned and processed.
FECG waveform shows the electrical activity of the baby’s heart inside the womb. Just like a normal ECG, it has three main parts:
•P-wave → shows the upper chambers of the heart (atria) contracting.
•QRS complex → shows the main pumping action of the heart (ventricles contracting).
•T-wave → shows the heart relaxing after each beat.
INTRODUCTION
WHAT IS FECG WAVEFORM ?
DEPARTMENT OF ELECTRONICS AND COMMUNICATION ENGINEERING, BHAGWAN PARSHURAM INSTITUTE OF TECHNOLOGY

## Slide 5
IMPORTANCE OF CONTINUOUS MONITORING
FECG gives doctors important information about the baby’s heart during pregnancy. It helps in detecting heart defects early, checking if the baby is under stress, and ensuring that the heart is developing normally. This makes it a very useful tool for safer pregnancies and better newborn health.
CLINICAL SIGNIFICANCE OF FECG
Continuous fetal ECG monitoring allows doctors to keep track of the baby’s heart in real time. It helps in spotting sudden changes, warning signs of distress, or irregular heartbeats. With early detection, doctors can act quickly, which reduces risks for both the mother and the baby and supports a safer delivery.
DEPARTMENT OF ELECTRONICS AND COMMUNICATION ENGINEERING, BHAGWAN PARSHURAM INSTITUTE OF TECHNOLOGY

## Slide 6
LITERATURE
SURVEY
DEPARTMENT OF ELECTRONICS AND COMMUNICATION ENGINEERING, BHAGWAN PARSHURAM INSTITUTE OF TECHNOLOGY

## Slide 7
SOLUTION PRESENTED
DEPARTMENT OF ELECTRONICS AND COMMUNICATION ENGINEERING, BHAGWAN PARSHURAM INSTITUTE OF TECHNOLOGY

## Slide 8
Fetal ECG System Workflow:
Data Acquisition:
  Abdominal electrodes capture maternal and fetal ECG signals
  AFE module amplifies and filters the signals
  Microcontroller receives the processed data
Data Pre-processing & Transfer:
  Digital filtering and noise removal are applied
  Data is transmitted via BLE, Wi-Fi, USB, or stored locally
AI Segmentation & Analysis:
  Pre-processed ECG is analyzed by ResNet and Transformer models
  Features are fused and classified
  Final output includes fetal ECG segmentation and heart rate estimation.
SOLUTION PRESENTED
DEPARTMENT OF ELECTRONICS AND COMMUNICATION ENGINEERING, BHAGWAN PARSHURAM INSTITUTE OF TECHNOLOGY

## Slide 9
COMPONENTS OR SOFTWARE USED
DEPARTMENT OF ELECTRONICS AND COMMUNICATION ENGINEERING, BHAGWAN PARSHURAM INSTITUTE OF TECHNOLOGY
Hardware Components :
  AD8232 ECG Sensor Module
  ESP32 Development Board (DOIT DevKit v1)
  3-Lead Ag/AgCl ECG Electrodes
  MicroSD Card Module (SPI Interface)
  MicroSD Card (32GB, Class 10)
  Micro-USB Cable
  USB Power Adapter (5V/1A)
  Breadboard (830-hole)
  Jumper Wires (Male-to-Male & Male-to-Female)
  Male Header Pins (40-pin)
  Female Header Pins (40-pin)
  Resistors (10kΩ, 1kΩ assortment)
  Capacitors (0.1µF, 10µF assortment)
AD8232 ECG SENSOR
ESP32 DEVELOPMENT BOARD
3-LEAD AG/AGCL ECG ELECTRODES
MICROSD CARD WITH MODULE
BREADBOARD (830-HOLE)
RESISTORS AND CAPACITORS

## Slide 10
COMPONENTS OR SOFTWARE USED
Software Components :
  Python
  PyTorch or TensorFlow
  Arduino IDE
  Kaggle
  Streamlit
  Pandas & NumPy
  Matplotlib & Seaborn
  Scikit-learn
  Git Hub
DEPARTMENT OF ELECTRONICS AND COMMUNICATION ENGINEERING, BHAGWAN PARSHURAM INSTITUTE OF TECHNOLOGY
PYTHON
PYTORCH
VS CODE
STREAMLIT
OPENCV
GIT
ARDUINO IDE
NUMPY
SEABORN
SCIKIT LEARN

## Slide 11
WORKING OF PROJECT
PHASE 1
DEPARTMENT OF ELECTRONICS AND COMMUNICATION ENGINEERING, BHAGWAN PARSHURAM INSTITUTE OF TECHNOLOGY
DATASET
  PhysioNet Challenge 2013 (75 records, 4-channel abdominal ECG)
  Sampling rate: 1000 Hz | Duration: 60 seconds/record
  QRS annotations provided (.fqrs) files.
SIGNAL PRE-PROCESSING
  Notch filter (50 Hz) → powerline noise removal
  Bandpass filter (0.5-100 Hz) → frequency range extraction
  Wavelet denoising (Symlet-10, Level 6) → artifact suppression
  Baseline correction → drift elimination
DATA ACQUISITION & PREPROCESSING
DATA ORGANIZATION AND OUTCOME
  Batch processing: 25 samples/batch
  Total: 4.5M preprocessed samples
  Outcome: Clean 4-channel ECG signals ready for analysis
PHASE 2
MATERNAL-FETAL ECG SEPARATION
OBJECTIVE
Isolate pure fetal ECG from mixed maternal-fetal abdominal signals
CHALLENGE
  Abdominal ECG contains superimposed maternal and fetal signals
  Maternal heart rate: 60-100 bpm (dominant amplitude)
  Fetal heart rate: 120-180 bpm (weaker amplitude)
  Requires signal separation while preserving morphology
APPROACH
  Source separation techniques for multi-channel recordings
  Frequency-based or blind source separation methods
  Component identification based on physiological characteristics
  Signal reconstruction maintaining cardiac waveform integrity

## Slide 12
PHASE 3
DEPARTMENT OF ELECTRONICS AND COMMUNICATION ENGINEERING, BHAGWAN PARSHURAM INSTITUTE OF TECHNOLOGY
ARCHITECTURE: Hybrid Deep Learning Model
  ResNet Blocks: Spatial feature extraction with skip connections
  Multi-Frequency CNN: Parallel kernels for multi-scale pattern capture​. Small kernels → QRS, Medium → T-wave, Large → P-wave
  Transformer Attention: Multi-head attention (4 heads) for P-QRS-T dependencies
  U-Net Decoder: Upsampling with skip connections for pixel-wise segmentation
  Output Classes: Class 0: Background
Class 1: QRS
Class 2: T-wave
  Performance: IoU: 85%
T-wave accuracy: 90%
Boundary precision: ±15ms
  Outcome: Precise P-QRS-T segmentation for morphological analysis
MORPHOLOGY EXTRACTION
PHASE 4
ARRHYTHMIA CLASSIFICATION
FEATURE EXTRACTION
  Heart rate, R-R intervals, HRV
  QRS duration, amplitude
  T-wave duration, amplitude
  QT interval, ST segment deviation
  QRS-T ratio, Corrected QT (QTc)
CLINICAL CRITERIA & CLASSIFICATION
  Long QT: >440ms | Short QT: <360ms
  Bradycardia: HR <110 bpm | Tachycardia: HR >180 bpm
  ST elevation: >0.1 mV | Irregular rhythm via HRV
  Algorithm: Ensemble machine learning methods
  Input: 15+ morphological features
  Output: Binary (Normal / Arrhythmic) + confidence score
OUTCOME & PERFORMANCES
  Accuracy: 92% | Sensitivity: 95% | Specificity: 90% | AUC: 0.94
  Validated arrhythmia detection system for clinical deployment

## Slide 13
Feature | Existing Solutions | Our Proposed Solution (Hybrid)
Analysis Engine | Monolithic Models: Often use a single U-Net (CNN) or a standard RNN/Transformer | Dual-Path Fused Model: 1. ResNet Path (Local Expert) 2. Multi-Frequency Transformer Path (Global Expert)
Feature Extraction | Local or Global: • U-Nets are strong at local waveform shape but miss long-range rhythm patterns. • RNNs are good at global time-series but weak on fine-grained signal morphology. | Synergistic (Local + Global): • ResNet Path captures the precise, fine-grained morphology (shape) of the P-QRS-T waves. • Transformer Path models the global, long-range dependencies and rhythm of the entire signal.
Noise Handling | Single-Scale Analysis: Standard models process the signal as a whole, making them vulnerable to noise across different frequencies (e.g., maternal muscle noise, baseline wander). | Multi-Frequency Analysis:Our Convolutional Transformer processes the signal at multiple frequencies simultaneously, allowing it to isolate the weak fetal signal from complex, multi-band noise.
Output | Primarily Fetal Heart Rate (FHR) estimation. Waveform segmentation is often less accurate. | High-Fidelity Segmentation Mask: Provides a precise, sample-by-sample segmentation of the fetal ECG, leading to more accurate heart rate estimation and morphological insights.
DEPARTMENT OF ELECTRONICS AND COMMUNICATION ENGINEERING, BHAGWAN PARSHURAM INSTITUTE OF TECHNOLOGY
COMPARISON WITH EXISTING SOLUTIONS

## Slide 14
FUTURE SCOPE
DEPARTMENT OF ELECTRONICS AND COMMUNICATION ENGINEERING, BHAGWAN PARSHURAM INSTITUTE OF TECHNOLOGY
Wearable Devices – Small, wireless patches for easy home use.
Smarter AI – Detects early risks and gives personalized care using big data.
1
2
3
4
5
Data Privacy – Safe methods (like federated learning) to protect patient info.
More Insights – Combine ECG with other signals for full picture of baby’s health.
Efficient Systems – Run powerful algorithms on low-power, portable devices.
6
Standardization – Common protocols and databases for better diagnosis in hospitals

## Slide 15
REFERENCES
  D. S. S. Chintapenta, A. Verma, and S. Majumder, “MFCONVTR: Multi-frequency Convolutional Transformer for Fetal Arrhythmia Detection in non-invasive FECG,” in Lecture notes in computer science, 2025, pp. 49–59. doi: 10.1007/978-3-031-87660-8_4
  S. Cao, H. Xiao, G. Gong, W. Fang, and C. Chen, “Morphology extraction of fetal ECG using temporal CNN-based nonlinear adaptive noise cancelling,” PLoS ONE, vol. 17, no. 12, p. e0278917, Dec. 2022, doi: 10.1371/journal.pone.0278917.
  E. Jing, H. Zhang, Z. Li, Y. Liu, Z. Ji, and I. Ganchev, “ECG heartbeat classification based on an improved RESNET-18 model,” Computational and Mathematical Methods in Medicine, vol. 2021, pp. 1–13, Apr. 2021, doi: 10.1155/2021/6649970
  Mohebbian, M. R., Vedaei, S. S., Wahid, K. A., Dinh, A., Marateb, H. R., & Tavakolian, K. (2021). Fetal ECG extraction from maternal ECG using Attention-Based CycleGAN. IEEE Journal of Biomedical and Health Informatics, 26(2), 515–526.
  L. Chen, S. Wu, and Z. Zhou, “Fetal ECG Signal Extraction from Maternal Abdominal ECG Signals Using Attention R2W-Net,” Sensors, vol. 25, no. 3, p. 601, Jan. 2025, doi: 10.3390/s25030601.
DEPARTMENT OF ELECTRONICS AND COMMUNICATION ENGINEERING, BHAGWAN PARSHURAM INSTITUTE OF TECHNOLOGY

## Slide 16
  Y. Yang, L. Chen, and S. Wu, “Enhancing Fetal Electrocardiogram Signal Extraction Accuracy through a CycleGAN Utilizing Combined CNN–BiLSTM Architecture,” Sensors, vol. 24, no. 9, p. 2948, May 2024, doi: 10.3390/s24092948.
  M. Alghieth, “DeepECG-Net: a hybrid transformer-based deep learning model for real-time ECG anomaly detection,” Scientific Reports, vol. 15, no. 1, Jul. 2025, doi: 10.1038/s41598-025-07781-1
  S. Ziani, “A Novel Approach for Detecting Fetal Electrocardiogram (FECG) Signals: Integration of Convolutional Neural Network (CNN) with Advanced Mathematical Techniques,” in Lecture notes in networks and systems, 2024, pp. 402–410. doi: 10.1007/978-3-031-53824-7_37.
DEPARTMENT OF ELECTRONICS AND COMMUNICATION ENGINEERING, BHAGWAN PARSHURAM INSTITUTE OF TECHNOLOGY

## Slide 17
THANK YOU
DEPARTMENT OF ELECTRONICS AND COMMUNICATION ENGINEERING, BHAGWAN PARSHURAM INSTITUTE OF TECHNOLOGY